## Slide 1
POE-Injector
Parman company
Mentor : Mrs. Shaterzade
Members : Mehrad Afshari Nazari, Arezoo Savlani

## Slide 2
01 02 03
04
PCB Design
05
Agile Working
TABLE Of CONTENTS
Schematic Design
Theory & Initial information
Introduction

## Slide 3
Introduction
01

## Slide 4
:
Project Overview and Objectives :
Project Description:
  This project involves the design of a plug-in electronic board that performs control and management functions for a main PoE injector board. The plug-in board includes a microcontroller responsible for generating and managing I2C signals to interact with and control the PoE controller chip on the main board , UART signals to communicating with a debugging and monitoring system and RMII signals for communicating with physical layer of network. The primary objective is to enhance the operational capabilities and streamline the control processes of the PoE injector system.
Goals and Objectives:
Develop a plug-in board capable of efficiently managing the PoE injector main board's operations.
Create a modular plug-in board that can be easily attached or detached from the main PoE injector board.

## Slide 5
Theory & Initial information
02

## Slide 6
:
A PoE injector (Power over Ethernet injector) is a device used to supply both data and electrical power to network devices through a single Ethernet cable. It allows devices like IP cameras, wireless access points, and VoIP phones, which require both data and power, to be connected to a network without needing separate power adapters.
PoE injector:

## Slide 7
Benefits:
Simplified installation
Single cable for data and power
No need for nearby power outlets
Flexible device placement
Reduced cable clutter
Cost-effective power solution
Easy network expansion
Supports remote devices (IP cameras, access points)
Safe and reliable power distribution
PoE standards compatibility (802.3af, 802.3at, 802.3bt)

## Slide 8
Block Diagram of main board

## Slide 9
:
3D model of PCB Board

## Slide 10
:
Keyword of contents:
Protocols : I2C,UART,RMII
Network models: OSI , TCP/IP
Cat5 cables , PoE Devices , PoE standards
NPI framework
UART communication standards : RS-232
debugging and programming interfaces : JTAG and SWD
Transformer and isolator ICs
eeprom
ferrite bead
fiducial

## Slide 11
Schematic Design
03

## Slide 12
01 02 03
04
Creating pages and placing components in related pages
05
Organizing and arranging pages by standard numbering
Steps of schematic design:
Preparing library of components
Choosing ICs based on needs and being available
Creating Block Diagram
Making connections between components with wires, labels, global nets ,bus and offpage connectors
06

## Slide 13
07
Steps of schematic design:
Creating netlist to finding out :
Different nets with similar name and vice versa
Adding essential components such as resistors, capacitors, ferrite beads based on application notes and electronic considerations
09
Creating DRS report to finding out :
Unconnected pins
Not allowed connections based on direction
…
Creating layout and sync with schematic
Annotating number of components
08
10
11

## Slide 14
Block Diagram of plug-in board

## Slide 15
MCU:
  STM32F765
  AT24C04D_SSHM_T(eeprom)
  JTAG
Communication Path: MAX3232EIPW Driver
Port: 2x10 Pin Male/Female Header
ICs
Ethernet Path
DP83848KSQ_NOPB
LP82453NL Transformer

## Slide 16
Standards
Try as much as you can to not use specific letter (/ or + or (Use underline instead of space)
Put numbers for your pages and parts.
Try not to use global nets with same voltage and different names.
Elements names(Page number + number or letter like R313: resistor 13 of page 3)
Name your design file with date of edit. (Like: POEICPT1_R1_2024_8_13_3)
:

## Slide 17
:
Final Design:
eeprom

## Slide 18
:
Final Design:
phy

## Slide 19
:
Final Design:
MCU

## Slide 20
:
Final Design:
MCU_POWER

## Slide 21
:
Final Design:
port

## Slide 22
:
Final Design:
RS-232 Driver/receiver

## Slide 23
:
Final Design:
JTAG

## Slide 24
PCB Design
04

## Slide 25
01 02 03
04
plane
Creating plane for voltage supplies
05
Match impedance
Calculating wire impedances with Polar and finding appropriate wire width
Steps of PCB design:
placement Placing components based on standard distances and determined places for screws and ports
library Preparing footprint libraries and setting layer stack-up
outline
Drawing outline and keepin shape based on determined dimensions and standard clearance edge
constraints
Creating net groups and adjusting their constraints
06

## Slide 26
10
simulation
07
Routing
Connecting pins and applying fanout when changing layers
08
DRC
Setting rules and fixing DRC errors.
Steps of PCB design:
09
Waive unnecessary DRCs

## Slide 27
:
- DISTANCE:
Between resistors : 20MILS
Between resistors and IC: 100 MILS
Between two SMD IC: 150 MILS
Between IC and Through whole: 200 MILS
Corner fiducials distance from outline corners : 3 mm
Standards of placement

## Slide 28
:
Example of placement

## Slide 29
:
Calculating wire impedance with Polar

## Slide 30
:
Final PCB Design - Savlani

## Slide 31
:
Final PCB Design - Afshari

## Slide 32
:
Example of simulation:

## Slide 33
:
Example of simulation:
47ohm source destination resistor after assigning pin module

## Slide 34
Agile Working
05

## Slide 35
Scrum master
Scrum Master: The Scrum Master is a key role within a Scrum team, serving as a facilitator and coach. They are responsible for ensuring that Scrum practices are properly implemented and followed. The Scrum Master helps the team by removing obstacles that may hinder progress, fostering an environment of collaboration and continuous improvement, and coaching team members on Scrum principles and practices. Their goal is to enhance the team's effectiveness and efficiency in delivering high-quality results.

## Slide 36
Product owner
Product Owner: The Product Owner is responsible for defining and managing the product backlog, which is a prioritized list of features, enhancements, and fixes for the product. They act as a liaison between the stakeholders (such as customers, users, and business leaders) and the Scrum team, ensuring that the team is working on the most valuable tasks. The Product Owner clarifies requirements, sets priorities, and makes decisions about what to build and when, aiming to maximize the product's value and meet stakeholder expectations.

## Slide 37
:
Example Kanon table:
Week1(Sprint 1&2) | To Do | Doing | Test and debug | Done
Savlani | -Instal cadence -Search about PoE -Finish proposals | -Installing cadence -Search about PoE -Writing proposals | Problem in zip file - - | No Yes Yes
Afshari | -Instal cadence -Search about PoE | -Clearing storage -Search about PoE | Problem in zip file - | No Yes
Mrs.Shaterzadeh | - Send educational content for cadence | - | - | Yes

## Slide 38
Thanks!